## Slide 1: Synthetic Histories
ARMA-ed and dangerous

## Slide 2: Motivation
Goal: Calculate meaningful impact over many time histories
Problem: Availability in existing year-to-year data
  Wind, solar, demand/load
  Short recorded history
  Missing portions of records
Need: Source of data
  Consistent time intervals
  Reflects real behavior
  Statistically significant (over 100k years)
Solution: Good synthetic histories
  Stochastic Modeling

## Slide 3: Why Stochastic Modeling
Problems with deterministic “real” dataset
  Small sample size
  Optimization converges on data, not phenomenon
Benefits of synthetic data
  Unbounded sample size
  Underlying behavior captured in large statistical sampling
  Allows probabilistic analysis of HES and stochastic optimization
Limitations of synthetic data
  Each evaluation should statistically conform to real-life data
  Each evaluation should be independent

## Slide 4: Stochastic Time Series Methods in literature
Artificial Neural Network
Factor Analysis
Gaussian Process
Power Spectrum Density
Numerical Weather Prediction
Autoregressive (AR)
Autoregressive Moving Averaging (ARMA)
Our approach:
  Data selection
  Fourier de-trending
  Residual normalization
  ARMA to represent the residuum

## Slide 5: Data Selection
We might not have enough data for stochastic optimization
But we might have more than one time period
Chart: 
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2
 | 7.6199e-24 | 1.1286e-19 | 6.221e-16 | 1.2798e-12 | 9.8659e-10 | 2.8665e-07 | 3.1671e-05 | 0.0013499 | 0.02275 | 0.15866 | 0.5 | 0.84134 | 0.97725 | 0.99865 | 0.99997 | 1 | 1 | 1 | 1 | 1 | 1
 | 2.8665e-07 | 3.3977e-06 | 3.1671e-05 | 0.00023263 | 0.0013499 | 0.0062097 | 0.02275 | 0.066807 | 0.15866 | 0.30854 | 0.5 | 0.69146 | 0.84134 | 0.93319 | 0.97725 | 0.99379 | 0.99865 | 0.99977 | 0.99997 | 1 | 1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.9067e-198 | 2.7536e-89 | 7.6199e-24 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0.00042906 | 0.0013499 | 0.0038304 | 0.0098153 | 0.02275 | 0.04779 | 0.091211 | 0.15866 | 0.25249 | 0.36944 | 0.5 | 0.63056 | 0.74751 | 0.84134 | 0.90879 | 0.95221 | 0.97725 | 0.99018 | 0.99617 | 0.99865 | 0.99957
1st period
2nd period
3rd period
Sub-period
Sub-period
Sub-period
Notes: Take the sub-period that is statistically closest to the average of all peers

## Slide 6: Data Selection Example (Wind)
Month | From Dataset of | Month | From Dataset of
January | 2005 | July | 2006
February | 2006 | August | 2006
March | 2004 | September | 2004
April | 2004 | October | 2004
May | 2006 | November | 2004
June | 2006 | December | 2005

## Slide 7: Fourier De-trending
Reconstructing the Signal
  Low frequencies
    represent a trend (season, day)
    Fourier is used
  High frequencies
    Statistical “noise”
Cases so far examined trends from 15 minutes to 1 year in period
Frequencies are user supplied
Moments are computed using least square linear regression

## Slide 8: De-Trending Results: Wind

## Slide 9: De-Trending Results: Load

## Slide 10: Reconstructing High Frequencies
“Noise” overlaid on Fourier trends (residuals)
The residuals are not normally distributed
Before the application of the ARMA need to “whiten” the noise
Reconstructing the full signal
Fourier Component
Original signal
CDF Residual
Inverse Normal CDF
Normal distributed residual

## Slide 11: ARMA Training
The normal distributed residuum is used to train an ARMA
The determination of the unknown parameters is based on the Maximum Likelihood Estimation (MLE)
The values of p, q are chosen using the Bayesian information criterion (BIC)

## Slide 12: Algorithm Layout

## Slide 13: Results Wind Speed
Statistics | Database | Synthetic
Mean (wind speed) | 8.078 | 8.088
Standard deviation (wind speed) | 3.392 | 3.372
Mean (step to step difference) | 0 | 0
Standard deviation (Step to step difference) | 0.659 | 0.642

## Slide 14: Results Load
Statistics | Database | Synthetic
Mean (wind speed) | 1102.3 | 1103.4
Standard deviation (wind speed) | 222.2 | 223.8
Mean (step to step difference) | 0 | 0
Standard deviation (Step to step difference) | 48.4 | 54.2

## Slide 15: CDF Comparison

## Slide 16: Scenario Generation

## Slide 17: Moving Forward

## Slide 18: Break
What we recently talked about:
  Synthetic time histories via ARMA
    Fourier modes
    Residuals
    Signal reconstruction
Coming up next:
  Practical ARMA application
    Real data
    Training
    Sampling
    Statistics

## Slide 19: Your turn …
Workflows
  Obtain training data
  Train ARMA
    Read in data
    Preprocess
    Train
    Serialize
  Sample ARMA
    Unserialize
    Sample
    Output
train_arma.xml
sample.xml
raven/docs/workshop/ARMA/exercise

## Slide 20: Hands-On: Obtaining Real Data
Find an online source of data (e.g. NREL)
Collect data into RAVEN-friendly form
  History set of linked CSVs
  Must have consistent time step throughout
  No time steps can be missing
  Each period must be identical in length
  Each period must have identical time stamps
  Example script:
  Example data (wind speeds near Idaho Falls from NREL):
  Example RAVEN-compatible data:
raven/docs/workshop/ARMA/raw_data/parse_nrel.py
raven/docs/workshop/ARMA/raw_data/101645-*.csv
raven/docs/workshop/ARMA/raw_data/raw_data*.csv

## Slide 21: Hands-On: Training ARMA Walkthrough
Read in data
TypicalHistory Preprocess
Train ARMA
Serialize ARMA
raven/docs/workshop/ARMA/exercise/train_arma.xml
<IOStep name=“readInData”>
<PostProcess name=“typicalHistory”>
<RomTrainer name=“train”>
<IOStep name=“serialize”>

## Slide 22: Hands-On: Training ARMA Exercises
Fill in the following:
RunInfo
  Sequence
DataObjects
  Input
  Output
  pivotParameter
Files
  Raw data file
  Serialized ARMA file
Typical History PostProcessor
  Subsequence length (1 day)
  Output Length (1 week)
  PivotParameter
ARMA ROM
  Target
  Features
  pivotParameter
raven/docs/workshop/ARMA/exercise/train_arma.xml
<!–- TODO ... -->
Each task is marked with a
After you finish, try running!
../../../../raven_framework train_arma.xml

## Slide 23: Hands-On: Sampling ARMA Walkthrough
Unserialize
Sample
Print/Plot
raven/docs/workshop/ARMA/exercise/sample_arma.xml
<IOStep name=“load”>
<MultiRun name=“sample”>
<IOStep name=“output”>

## Slide 24: Hands-On: Sampling ARMA Exercises
After you finish, try running!
Each task is marked with a , ignore
Fill in the following:
RunInfo
  Sequence
DataObjects
  Input
  Output
  pivotParameter
Files
  Serialized ARMA file
Samplers
  Number of Samples
  Seed
ARMA ROM
  Target
  Features
  pivotParameter
raven/docs/workshop/ARMA/exercise/sample_arma.xml
<!–- TODO -->
../../../../raven_framework sample_arma.xml
<!–- EXTRA -->

## Slide 25: Hands-On: Sampling ARMA Results
Note: depends on your seed, number of samples
  I used seed = 31415 with 3 samples
raven/docs/workshop/ARMA/exercise/rundir/samples_plot_line.png

## Slide 26: Hands-On: Running Some Statistics
Calculate and plot the mean and 5,95 percentiles for samples
  Same input file
  Create a new PostProcess step
    Input is the history set
    Model is the ”stats_calc” postprocessor
    Output is data object “stats”
  Create a new Output step
    Input is “stats” data object
    Output is outstream print “stats_out”
  Add both steps to the RunInfo sequence
  Each task is marked with a
  Better stats: increase the number of MonteCarlo samples (>50)
<!–- EXTRA -->
sample_arma.xml

## Slide 27: Hands-On: Statistics Results
50 MC samples, seed 31415, percentile 5|95 and mean

## Slide 28: Hands-On: Beyond the Scope
Other things to try
  Run it in local parallel
    RunInfo: batchSize, maxQueueSize
  Compare stats at 10 samples and 1000 samples
  Start over with new ARMA
    Change subsequence length (maybe 1 week)
    Change output length (1 month or 1 year)
    Change number of interpolation points on plots if needed